Lowcountry Storm Panels – Sheet Cutting Worksheet (Print as many of these worksheets as you need)

# Note: Internal flutes in sheets run vertically. Although it is desirable to plan your cuts so that, after cutting, the flutes will remain vertical once the panel is mounted (to promote drainage), it is not mandatory and is primarily a cosmetic concern. If, in order to reduce waste when planning the cutting, you elect to cut some panels so that when mounted their internal flutes run in the horizontal orientation it is acceptable and has no bearing on strength.

Using a pencil, draw outlines of the panels desired on the full sheet templates below (don’t worry about scale) and indicate their dimensions. Full sheets are available in 48”x72”, 48”x96”, 48”x120”, 72”x60”, 72”x72”, 72”x96” and 72”x120” sizes. If these instructions are unclear to you, please let us know and we will fax you a completed example. While every attempt will be made to cut your order as precisely as possible, please note that cutting tolerances may be plus or minus 1/8”.

The rectangle below represents a full			The rectangle below represents a full

sheet that is _______” x _______”			sheet that is ______” x ______”